## Slide 1: Lessons learnt in ground-based instruments
Julien Milli
Notes: Biased towards VLT instruments bc spent many years @ VLT

## Slide 2: Outline
What is currently limiting us ?
What have we learnt ?
Perspectives

## Slide 3: First generation AO systems
VLT/NaCo PSF at H band (1.6mm), saturated in the center
Asymmetric halo
Speckles with various timescales: dynamical and quasi-static poorly averaging with time
AO correction driving the design, not so much the temporal stability, critical to calibrate the stellar residuals (no pupil stabilisation initially, varying flexures of the instruments…)
Coronagraphy only starting
 limited contrast
Notes: Many of you have probably never worked with 1st gen AO systems

## Slide 4: Second generation high-contrast instruments
1st gen on steroids with a highlight on
Stability
Diffraction control and coronagraphy
Dedicated low-order WFS or NCPA calibration strategies
Dedicated observation strategies to allow differential imaging
Post-processing considered at instrument design
 The contrast is the new metrics rather than the Strehl ratio
VLT/SPHERE coronagraphic images at H band (1.6mm)
cf Tuesday talk by F. Cantalloube and B. Jansen-Clem
Notes: A lot of promises: we’ll be able to forget about the atmosphere, turbulence will be perfectly corrected on bright stars

## Slide 5: Strehl distribution
Recall Strehl Ratio
For bright stars in good conditions, the floor of 90% Strehl is reached !
Still some work to do to increase the performance on stars fainter than G~7 and to reach stars > 14 mag
Coherence time is critical !
Chomez et al. submitted
VLT/SPHERE (SHINE survey on 400 targets, visitor mode)
Strehl
Magnitude V
Milli et al. 2017

## Slide 6: Conditions do matter
At the VLT, coherence time and seeing are jointly used as QC parameter (one of the 1st lessons from VLT/SPHERE operations)
Significant implications for detection / non-detection of a candidate
Drives the need for accurate turbulence predictions (e.g. Masciadri et al. 2023)
Turbulence conditions
top 70%
top 50%
top 30%
VLT/SPHERE (SHINE survey on 400 targets, visitor mode)
(H band)
Chomez et al. submitted

## Slide 7: Conditions do matter
  Signal-to-noise maps of the 5 MJup planet 51 Eri b (Macintosh et al, 2015) observed on 4 epochs (Samland et al. 2017, Brown-Sevilla et al. 2023)
Various S/N despite similar Strehl 80-90%
S/N

## Slide 8: Contrast distribution
Even at high Strehl, the contrast can vary by an order of magnitude
Strehl = integrated quantity that does not describe the PSD of the aberrations or the coronagraph centering
Raw contrast in the H band vs H mag (VLT/SPHERE SHINE survey)
Chomez et al. submitted
(H band)
+ + + +
Recall: for rad2: (Marechal approximation)

## Slide 9: Contrast curves
The contrast curve is the key to decipher what is limiting the performance
VLT / SPHERE / IRDIS contrast from the SHINE survey
Top 30%
Top 50%
Top 85%
+ + + +
Chomez et al. submitted

## Slide 10
ALIASING
FITTING
LOW ORDERS
SERVOLAG
Curve adapted from Kasper et al. 2012, images from Cantalloube et al. 2019
cf Monday talk by I. Lagina
N/2 l/D
Notes: perfect coronagraph with pure servolag/low order/aliasing/fitting

## Slide 11: Fitting error
+ + + +
 maximize the number of actuators N (e.g. SPHERE with 41x41 actuators)
With N = Nact x Nact actuators one can correct Nact/2 cycles/pup:
Highest spatial frequency one can correct for
Coronographic images
l
Nact/2 l/D
J
H
K

## Slide 12: Aliasing error
+ + + +
Possible solution: spatially-filter SH WFS
One filter spatial frequencies higher than fs/2 upstream of the WFS
Spatial filter progressively closed
Fusco et al. 2014
Spatial filter
Recall what is aliasing in signal processing
With a finite sampling frequency fs, a signal of frequency f>fs/2 is seen as a signal with a frequency f-fs/2
Fusco et al. 2016

## Slide 13: Servolag and wind-driven halo
+ + + +
Movie from VLT / SPHERE (Credit J. Milli)
Black arrow is the jet stream wind direction

## Slide 14: Servolag and wind-driven halo
+ + + +
Movie from VLT / SPHERE (Credit J. Milli)
Black arrow is the jet stream wind direction Red arrow is the ground wind direction

## Slide 15: Servolag and wind-driven halo: pinning down the culprit
Madurowicz et al. 2018

## Slide 16: Servolag and wind-driven halo
+ + + +
Other evidence from high-altitude winds: asymmetric butterfly pattern (Cantalloube et al. 2018)
Mitigation strategies:
  Higher loop frequency (e.g. Subaru @3.6kHz, future SAXO+ @3kHz)
  Predictive control algorithms
  Choose well your observing slot
Residual phase (pupil plane)
Focal plane coronagraphic image

## Slide 17: Servolag and wind-driven halo
+ + + +
Other evidence from high-altitude winds: asymmetric butterfly pattern (Cantalloube et al. 2018)
Mitigation strategies:
  Higher loop frequency (e.g. Subaru @3.6kHz, future SAXO+ @3kHz)
  Predictive control algorithms
  Choose well your observing slot
All months are not equal
Monthly averaged wind speeds @VLT
January-March are far better in Chile

## Slide 18: Servolag and wind-driven halo
200mbar wind rose @ VLT (color=speed, radius=occurence in %)
Caution with E-W edge-on disks !
+ + + +
Other evidence from high-altitude winds: asymmetric butterfly pattern (Cantalloube et al. 2018)
Mitigation strategies:
  Higher loop frequency (e.g. SCeXAO @3.6kHz, MagAO-X @2-4kHz, future SPHERE+ @3kHz)
  Predictive control algorithms
  Choose well your observing slot
All months are not equal
All directions are not equal

## Slide 19: WFS photon noise
For faint stars, becomes the dominant term  Sensitive cameras are favoured (EMCCD on most instruments including GPI2.0)
Noise propagation is not the same for all WFS (Guyon et al. 2005)  Pyramid WFS are favoured, with a higher sensitivity to low-order aberrations: SCeXAO, MagAO, KPIC Baseline for GPI2.0, SPHERE+ 2nd stage AO
To reach redder and fainter stars, sensing in the NIR is favoured
+ + + +
SPHERE+ white paper, Boccaletti et al. 2021
R magnitude
# known protoplanetary disks
cf Tuesday talk by B. Jansen-Clem
Notes: As shown previously, perf degrades for fainter star

## Slide 20: Specific calibration problems: low wind effect
+ + + +
Factor 50
Contrast degradation up to a factor 50, affecting the best nights !

## Slide 21: Specific calibration problems: low wind effect
+ + + +

## Slide 22: All telescopes are not equal
Keck II
VLT UT3
Gemini South
Magellan (Clay)
Subaru
Spider design makes a clear difference

## Slide 23: Mitigation strategies
Software solutions: use of a dedicated modal basis for AO control, pupil piston/tip/tilt (Pourré et al. 2023)
Focal plane WFS (e.g. N’diaye et al. 2018, Vievard et al. 2019, Bos et al. 2020)
Courtney-Barrer et al. 2023
Coated spider
Uncoated spider
M2 tower
Low-emissivity coating applied between August and November 2017
Picture: P. Bourget
Milli et al. 2018

## Slide 24: Specific calibration problems: low wind effects
+ + + +
Illusive disk of HD206893 (Milli et al. 2017)
Beware of misinterpretation

## Slide 25: NCPA
Internal source
Vigan et al. 2019,2022
~45nm RMS
~35nm RMS
N’Diaye et al. 2016
Residual wavefront
Example of a NCPA calibration strategy with the Zernike WFS
+ + + +
cf Tuesday talk by B. Jensen-Clem

## Slide 26: Focal plane techniques to make a dark hole
Dark hole techniques do work on-sky in good conditions (when quasi-static speckles limit the contrast rather than the turbulence)
Mazoyer et al. 2024, Potier et al. 2020,2022
cf Tuesday talk by B. Jensen-Clem

## Slide 27: Lessons learnt in observing strategy and postprocessing
Notes: You’ve done your best in hardware, what else can you do?

## Slide 28: Use of telemetry data
AO telemetry data carry information about residuals statistics, hence the PSF:
  PSF reconstruction (from Véran+ 1997 to now, e.g. Fetick et al. 2019)
  Or support to deconvolution : relevant priors are beneficial (e.g. Lau et al. 2023)
Use in high contrast scenes ?
  Active field of research
  Relation between AO internal data and ultimate contrast performance not trivial
Deconvolved images of Vesta
Dawn model
Fetick et al. 2019

## Slide 29: Revisited strategies: Reference differential imaging
A) (Carefully selected) Single reference
  similar visual magnitude for AO performance
  close on sky and in time
  similar turbulence conditions
B) Large library of references
  Needs a large set of images available
  No additional observing time required
  Needs to identify the subset of adequate targets
Xie et al. 2023

## Slide 30: Single reference differential imaging: star hopping
Telescope pointing A
Telescope pointing B
Example with SPHERE IRDIS on a binary system with 9” separation and similar R magnitude
Combined offset done at the telescope  fast transition between A and B less than 20s (best case)
Duty cycle of 2min20

## Slide 31: Single reference differential imaging: results
b Pic b shortest separation IFS detection (ADI, 2.5h)
Contrast 1.5.10-4
Separation 125mas
Lagrange et al. 2018
Simulated planet of 2.10-5 contrast at 150mas
SPHERE Manual
Star hoping (1.5h)
Fake planet
Wahhaj et al. 2021

## Slide 32: The contrast floor in polarimetry
Contrast typically limited by photon noise from 0.5 arcsec (depending on conditions) up to the RON / background limit
PDI is very efficient because of the differential imaging is simultaneous
Typical contrast curve in PDI with VLT/SPHERE (45min on-source)
IRDAP, Van Holstein et al. 2020

## Slide 33: The contrast floor in optical polarimetry
Best contrasts on a Cen B with SPHERE / Zimpol (2h observations)
  0.2''-0.4'': ~3.10-7
  0.6''-0.8'': ~3.10-8
  > 1.0'': ~1.10-8
Separation in arcsec
Hunziker et al. 2020
Schmid et al. 2018

## Slide 34: Post-processing is key
A dedicated processing center (e.g. High Contrast Data Center) is very beneficial.
It combines in the same place all information relevent for signal extraction and interpretation
  environmental data from the observatory or beyond (GCM)
  Telemetry and engineering data
  Science and calibration data
It allows efficient building of reference library for RDI
cf Tuesday talk by F. Cantalloube
Obs night summary as seen from SPHERE telemetry
Notes: Data center: does not replace instrument expertise and pipelines or ESO archive, but build on them and with benefit to them

## Slide 35: Take home messages
Many contrast killers in current XAO instruments but those 2 are probably the most limiting
Dedicated observing strategies or postprocessing can mitigate many of those current limitations
Upgrades are on-going to tackle remaining limitations and act as demonstrators for future XAO on ELTs.
Wind-driven halo
Low-order aberrations
Cantalloube et al. 2019

## Slide 36: Upgrades coming or already on-sky
XAO systems are sensitive to very fine effects poorly known/studied before
  in the atmosphere (evolution of high-altitude wind, outer scale pattern…)
  in the dome (enhanced dome seeing due to global warming, low-wind effects, vibrations)
Servolag is a main contributor to error at small separations  upgrades with higher loop frequency and predictive control
Focal plane techniques will be key to further dig the contrast and remove remaining instrumental speckles at short separation
New parameter space also for fainter and redder targets

## Slide 37: 2030 horizon
Challenge : diffraction and wavefront control strategy over large, segmented, heavily obscured apertures
First-light instruments will have one HC mode (among others)

## Slide 38: Backup slides

## Slide 39: Star magnitude distribution
G magnitude