## Slide 1: Designing a coronagraphic system
Sagan Summer Workshop 2024
Advances in Direct Imaging: From Young Jupiters to Habitable Earths

## Slide 2: Contrast in Direct Imaging
What sets the fundamental limit for high-contrast imaging?
We usually specify “contrast”…
Astrophysical oriented metric | Instrument oriented metric
G2 star and Earth | ExAO raw contrast to
M6 star and Earth | Post-processed contrast to
Astrophysical oriented metric | Instrument oriented metric

## Slide 3: Problems with contrast
“Contrast” has several meanings
  “astrophysical flux ratio” is the planet to star flux ratio
  “raw contrast” is just an instantaneous intensity ratio in an image
  “post-processed contrast” is the sensitivity after image post-processing
The main problem: contrast is not a noise model
  A perfectly static background would not be a problem we could just subtract it.

## Slide 4: Problems with contrast
“Contrast” has several meanings
  “astrophysical flux ratio” is the planet to star flux ratio
  “raw contrast” is just an instantaneous intensity ratio in an image
  “post-processed contrast” is the sensitivity after image post-processing
The main problem: contrast is not a noise model
  A perfectly static background would not be a problem we could just subtract it.
The stellar PSF is the background here.

## Slide 5: Why do we need a coronagraph?

## Slide 6: Why do we need a coronagraph?

## Slide 7: Why do we need a coronagraph?

## Slide 8: Why do we need a coronagraph?
I changed the colormap scales to highlight the planet.

## Slide 9: Why do we need a coronagraph?
We found the planet. Easy right?

## Slide 10: Quantization of the electric field.
Classical electromagnetism tells us that the electric field is continuous.

## Slide 11: Quantization of the electric field.
Classical electromagnetism tells us that the electric field is continuous.

## Slide 12: Quantization of the electric field.
Classical electromagnetism tells us that the electric field is continuous.
But then Quantum Mechanics came along and quantized the electric field!

## Slide 13: Poisson noise (or shot noise)
photons / frame
photons / frame
photons / frame

## Slide 14: Model PSF subtracted
photons / frame
photons / frame
photons / frame

## Slide 15: The photon noise limit
If we had uncorrelated photon noise:

## Slide 16: The photon noise limit
If we had uncorrelated photon noise:
Then the S/N of the planet would be:

## Slide 17: The photon noise limit
If we had uncorrelated photon noise:
Then the S/N of the planet would be:

## Slide 18: Direct imaging photon noise limits
I am assuming a 6.5m aperture

## Slide 19: Direct imaging photon noise limits
I am assuming a 6.5m aperture

## Slide 20: Direct imaging photon noise limits
I am assuming a 6.5m aperture

## Slide 21: Direct imaging photon noise limits
I am assuming a 6.5m aperture

## Slide 22: Direct imaging photon noise limits
I am assuming a 6.5m aperture

## Slide 23: Aberration-free perfect coronagraphy
Detecting an Earth-like planet with high SNR is possible within 15 minutes if the incoming wavefront is without any aberration!
This is the fundamental limit set by astrophysics!

## Slide 24: Aberration-free perfect coronagraphy
Detecting an Earth-like planet with high SNR is possible within 15 minutes if the incoming wavefront is without any aberration!
This is the fundamental limit set by astrophysics!
However, we will never have a system free of other noise sources.

## Slide 25: What noise sources do we expect?
Anything that modifies the state of the wavefront will introduce stellar leakage into the coronagraph.
This means that the instrument environment matters!

## Slide 26: What noise sources do we expect?
Anything that modifies the state of the wavefront will introduce stellar leakage into the coronagraph.
This means that the instrument environment matters!
Ground-based telescope
Space-based telescope
Credit: ESO
Credit: NASA

## Slide 27: Telescope and instrument vibrations

## Slide 28: High-contrast imaging noise regimes
Perfect PSF subtraction. Now we average photon noise.
Imperfect PSF subtraction. Now we average speckle noise.

## Slide 29: Impact of wavefront aberrations
  Apply a small phase Taylor expansion
  The coronagraph removes the unaberrated component
  Propagate to the focal plane with a Fourier transform

## Slide 30: Sinusoidal aberration
Let’s analyze OPD errors instead of phase errors
Important scaling relations:

## Slide 31: Requirements for contrast

## Slide 32: Requirements for contrast
A sinusoid with unity power has a Fourier transform with unity power (Parseval's theorem!)

## Slide 33: Requirements for contrast

## Slide 34: Requirements for contrast
We need picometer wavefront errors to achieve contrast!

## Slide 35: Quantization errors and DMs
Quantization due to Digital Analog Converters (DAC) limits the precision with which we can move actuators on DMs.
Limited accuracy on the surfaces we can apply.
Ruane et al. 2020

## Slide 36: Quantization errors and DMs
Remember picometer precision required for 1e-10 contrast!
Number of bits in a DAC determine our precision.
Ruane et al. 2020

## Slide 37: Sources of wavefront errors
Telescope vibrations
Thermal deformation of the telescope + instrument
Internal wavefront errors from imperfect systems
Chromatism between the wavefront sensing channel and the science channel
Atmospheric turbulence
Atmospheric dispersion
Dome seeing
Water vapor content (IR)
Thermal background
Common environmental issues
Ground-based issues
Space-based issues
Micro-meteorites
Changing thermal radiation (Sun)
Degradation of coatings over time
Pico-meter stability requirement

## Slide 38: Contrast budget
During the design of a coronagraphic imager we need to balance these terms.

## Slide 39: Contrast budget

## Slide 40: Contrast budget
Stellar angular diameter
Star brightness
Exozodiacal dust
Unknown orbital motion

## Slide 41: Contrast budget
Stellar angular diameter
Star brightness
Exozodiacal dust
Unknown orbital motion
Segment phasing errors
Thermal wavefront errors
Atmospheric turbulence
Chromatic wavefront errors

## Slide 42: Contrast budget
Stellar angular diameter
Star brightness
Exozodiacal dust
Unknown orbital motion
Segment phasing errors
Thermal wavefront errors
Atmospheric turbulence
Chromatic wavefront errors
Read noise
Dark current
Charge transfer noise
Detector saturation

## Slide 43: Contrast budget
Stellar angular diameter
Star brightness
Exozodiacal dust
Unknown orbital motion
Segment phasing errors
Thermal wavefront errors
Atmospheric turbulence
Chromatic wavefront errors
Read noise
Dark current
Charge transfer noise
Detector saturation
Almost nothing we can do about this.
Better wavefront control and sensing.
Develop better detectors.

## Slide 44: Local convection

## Slide 45: Global convection
Credit: NASA/wikipedia

## Slide 46: Adaptive optics is necessary
Atmospheric turbulence is created by convection in the atmosphere
This creates pockets of air with different temperatures that drift over the telescope.
Air with a different temperature also has a different refractive index.
Pi Pup at z’ with MagAO-X
credit: J. Long & B. Mazin

## Slide 47: Adaptive optics

## Slide 48: Adaptive optics
Wavefront sensor

## Slide 49: Adaptive optics
Wavefront sensor
Real-time Computer

## Slide 50: Adaptive optics
Wavefront sensor
Real-time Computer

## Slide 51: Adaptive optics is necessary
Atmospheric turbulence is created by convection in the atmosphere
This creates pockets of air with different temperatures that drift over the telescope.
Air with a different temperature also has a different refractive index.
Pi Pup at z’ with MagAO-X
credit: J. Long & B. Mazin

## Slide 52: Wavefront errors
Let’s dive a little bit deeper into the wavefront errors.
Wavefront errors have a particular lifetime .

## Slide 53: Wavefront errors
Let’s dive a little bit deeper into the wavefront errors.
Wavefront errors have a particular lifetime .
That means that we don’t have the expected scaling, but a . The lifetime of a speckle matters!

## Slide 54: Wavefront errors
Let’s dive a little bit deeper into the wavefront errors.
Wavefront errors have a particular lifetime .
That means that we don’t have the expected scaling, but a . The lifetime of a speckle matters!
10
Males et al. 2021

## Slide 55: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021
It’s speckle lifetime!

## Slide 56: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021

## Slide 57: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021

## Slide 58: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021
The static diffraction pattern of the instrument ()
Long-living quasi-static speckles (>1 minute to hours)
Short-lived atmospheric speckles (5 ms to 100 ms)

## Slide 59: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021
The static diffraction pattern of the instrument ()
Long-living quasi-static speckles (>1 minute to hours)
Short-lived atmospheric speckles (5 ms to 100 ms)
Either reduce the speckle strength ()
or
reduce their lifetime ()

## Slide 60: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021
The static diffraction pattern of the instrument ()
Long-living quasi-static speckles (>1 minute to hours)
Short-lived atmospheric speckles (5 ms to 100 ms)
Either reduce the speckle strength ()
or
reduce their lifetime ()
Active control of wavefront aberrations at all planes reduce all terms!

## Slide 61: Can we arbitrarily speed up?
The speed of an AO system should be faster than the speckle lifetime! Otherwise you will never correct the speckles before they disappear.
But within a certain timeframe we only collect so many photons.
Correction speed is a trade off between correction speed and measurement noise (photon noise)!

## Slide 62: Can we arbitrarily speed up?
The speed of an AO system should be faster than the speckle lifetime! Otherwise you will never correct the speckles before they disappear.
But within a certain timeframe we only collect so many photons.
Correction speed is a trade off between correction speed and measurement noise (photon noise)!

## Slide 63: Rapidly changing atmosphere
Long coherence time
Cantalloube et al. 2020

## Slide 64: Rapidly changing atmosphere
Long coherence time
Short coherence time
Cantalloube et al. 2020

## Slide 65: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021
The static diffraction pattern of the instrument ()
Long-living quasi-static speckles (>1 minute to hours)
Short-lived atmospheric speckles (5 ms to 100 ms) (much small than NCPA).

## Slide 66
Credit: J. Long

## Slide 67: Non-common path aberrations
Males et al. in prep.
Limit achievable Strehl ratio
Cause stellar leakage into the coronagraph
Slowly change and are difficult to suppress with post-processing.

## Slide 68: Who will win the AO control battle?

## Slide 69: Who will win the AO control battle?
VS

## Slide 70: Who will win the AO control battle?
VS

## Slide 71: MagAO-X – Multi-stage adaptive optics
Woofer
ALPAO-97
Tweeter
BMC-2K
NCPA DM
BMC-1K
LOWFS
Speckle Control
Pyramid WFS
Loop speed <3.6 kHz
offload
AO Loop
Coronagraph Loop

## Slide 72: Focus Diversity Phase Retrieval

## Slide 73: Focus diversity Phase retrieval
After FDPR correction
Theoretical PSF
with 6.7mas jitter

## Slide 74: iEFC on-sky for the first time
Haffert et al. in prep

## Slide 75: iEFC on-sky for the first time
Haffert et al. in prep

## Slide 76: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021
The static diffraction pattern of the instrument ()
Long-living quasi-static speckles (>1 minute to hours)
Short-lived atmospheric speckles (5 ms to 100 ms) (much small than NCPA).

## Slide 77: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021
The static diffraction pattern of the instrument ()
Long-living quasi-static speckles (>1 minute to hours)
Short-lived atmospheric speckles (5 ms to 100 ms) (much small than NCPA).
High-contrast imaging is a constant battle against noise limits.

## Slide 78: What sets the limit of HCI?
Soummer et al. 2007
Males et al. 2021
The static diffraction pattern of the instrument ()
Long-living quasi-static speckles (>1 minute to hours)
Short-lived atmospheric speckles (5 ms to 100 ms)

## Slide 79: What sets the limit of HCI?
Soumer et al. 2007
Males et al. 2021
The static diffraction pattern of the instrument ()
Long-living quasi-static speckles (>1 minute to hours)
Short-lived atmospheric speckles (5 ms to 100 ms)

## Slide 80: What sets the limit of HCI?
Soumer et al. 2007
Males et al. 2021
is the efficiency of a photon-noise limited post-processing technique
is the throughput of the science instrument.

## Slide 81: What sets the limit of HCI?
Soumer et al. 2007
Males et al. 2021
is the efficiency of a photon-noise limited post-processing technique
is the throughput of the science instrument.
Reduce the speckle strength ()
Active control of wavefront aberrations at all planes reduce all terms!

## Slide 82: Example: time to reach SNR=5
Residual speckles at the level with a coherence time of 10 ms and a planet contrast of .
Ground-based (speckle limited)

## Slide 83: Example: time to reach SNR=5
Residual speckles at the level with a coherence time of 10 ms and a planet contrast of .
Ground-based (speckle limited)
Residual speckles at the level and a planet contrast of . Around a 5th magnitude star.
Space-based (photon noise limited)

## Slide 84: Where are we?
Credit: Vanessa Bailey

## Slide 85: Where are we?
Credit: Vanessa Bailey
Ground-based ELTs

## Slide 86: Where are we?
Credit: Vanessa Bailey
Spaced-based HWO
Ground-based ELTs

## Slide 87: Speckle origins – temporal drifts
Low-wind effect
Differential NCPA between on-sky and internal source
On-sky we see difference in NCPA.
We need on-sky NCPA correction.
Appears in low-wind conditions.
Interaction of thick spiders and temperature gradients that creates modes that are not well sensed by the AO system.
Vigan et al. 2019
Vigan et al. 2022
Sauvage et al. 2015
Pourre et al. 2022
We will need to measure NCPA on-sky
Internal turbulence can become significant.

## Slide 88: Speckle origins – temporal drifts
Polarization aberrations - SPHERE
Millar-Blanchaer et. al 2022
Schmid et al. 2018
Polarization aberrations - GPI

## Slide 89: Speckle origins – vibrations
Vibrations are the main challenge for small-IWA coronagraph.
Many vibrations come from the telescope.
Lozi et al. 2016

## Slide 90: Chromatic wavefront errors
Guyon et al. 2017

## Slide 91: The era of ELTs
Giant Magellan Telescope
Extremely Large Telescope
Thirty Meter Telescope
39.4 m
30.0 m
25.0 m

## Slide 92: Segmented apertures

## Slide 93: GMT – GMagAO-X
Males et al. 2024 Close et al. 2024 Haffert et al. 2024
There is a talk on GMagAO-X on Friday by Dr. Jared Males!

## Slide 94: Conclusion
You need to make a noise model to understand which aspects actually make an impact on your instrument design. This also requires you to understand how the data will be reduced!
Active wavefront control will always improve sensitivity and it is the main path towards more efficient planet imaging and characterization.
The stability of the instrument will limit our calibration capabilities both for wavefront sensing and post-processing.
There are no free lunches! Instrument design is a trade off.